## Slide 1: SSD To Solve The I/O Bottleneck
Iri Trashanski
Director, Business Development
SanDisk

## Slide 2: What Is A Solid State Drive?
A Solid State Drive (SSD) is a data storage device that uses flash media to store data, instead of the spinning platters found in mechanical hard disk drives
SSD Benefits
Reliability and Durability
Mobility
Performance
Improved user experience
Gartner, Jo Unsworth
December, 2006

## Slide 3: When Random and Sequential Are Used?
Random
  OS changes and updates
    A single DLL is generally 5 to 6 Disk Locations (min)
      Directory, MFT Entry, and other File System Metadata
      PE Hdr page, .text pages, .data pages, .rsrc pages, etc.
  Applications and documents changes and updates (on-the-go)
  Access user data
Sequential
  Boot
  Hibernate
  Application load (main file)
For example:
When opening an application, the data files will be read in a sequential manner, however, all the associated DLL’s (~100 in average) will be read and loaded in random from 5-6 disk locations per DLL.

## Slide 4: HDD Performance Is Not About Transfer Rate But IOPS!
HDD transfer time = Interface transfer + media transfer + mechanical latency (in ms!)
  For a typical 4KB request, the mechanical impact at the HDD level accounts for ~95% of the entire transfer!
  Transfer time accounts for a fraction of actual disk access time
Operating System (OS) transfers
  Random read
  Sequential read
  Random write
  Sequential write
Random read operations accounts for more than 50% of the OS transfers
Major effect on machine behavior

## Slide 5: 4KB Read is 50% of the read transfers
IOPS

## Slide 6: HDD vs. SSD Seek and Latency
Average Access Time = Ave. Seek Time + Latency Time/2
Average Access Time = 12 msec + 5 msec ~ 17 msec (5400rpm)
Access time is fixed to 0.11ms

## Slide 7: HDD Versus SSD
Model | SSD | HDD SATA 2.5’ 80GB
Transfer Rate: |  | 
Interface rate | 150 MB/s | 150 MB/s
Maximum Internal* | R : 67 MB/sec* W: 47 MB/sec* | R : 28 – 44 MB/sec* W: 28 – 44 MB/sec*
IOPS | 512B transfer size** R: 7430 | 512B transfer size** R: 68
IOPS | 4KB transfer size** R: 5405 | 4KB transfer size** R: 67
Read Seek Time: |  | 
Track-to-track | 0.11ms* | 3ms*
Average | 0.11ms* | 17ms*
Maximum | 0.15ms* | 33ms*
7
* Based on H2BENCHW 3.6
** Based on IOMETER 2003.12.16

## Slide 8: SSD vs. HDD IOPS
x80
Based on IOMETER 2003.12.16

## Slide 9: User Scenario Benchmarks
Conducted on Dell Latitude D420/D620 notebook

## Slide 10: SSD Boot
demo

## Slide 11: SSD Boot
demo

## Slide 12: MLC Meets PC Market Requirements
Double Density
High Performance
High Endurance
Lower price point
High performance
  Random Read
    Minimal degradation
    80x better than HDD
Endurance
  Supporting user scenarios
  Exceed PC OEM requirements
  Unlimited read
Field proven – mobile handsets and CE devices

## Slide 13
Thank You !